CpE6110

Homework #1

•	Discuss about the advantage(s) and the disadvantages of the von Nuemann concept.

•	A 40-MHz processor was used to execute a benchmark program with the following instruction mix and clock cycle counts:

| Instruction type | Instruction count | Clock cycle count |
| --- | --- | --- |
| Integer arithmetic | 45000 | 1 |
| Data Transfer | 32000 | 2 |
| Floating point | 15000 | 2 |
| Control Transfer | 8000 | 2 |

Determine the effective CPI, MIPS rate, and execution time for this program.

•	A workstation uses a 15-MHz processor with a claimed 10-MIPS rating to execute a given program mix.  Assume a one-cycle delay for each memory access:

a)	What is the effective CPI of this computer?

b)	Suppose the processor is being upgraded with a 30-MHz clock.  However, the speed of the memory subsystem remains unchanged, and consequently two clock cycles are needed per memory access.  If 30% of the instructions require one memory access and another 5% require two memory accesses per instruction, what is the performance of the upgraded processor with a compatible instruction set and equal instruction counts in the given program mix?

•	Three enhancements with the following speedups are proposed:

Speedup1 = 30

Speedup2 = 20

Speedup3 = 10

Only one enhancement is usable at a time:

- If enhancements 1 and 2 are each usable for 30% of the time, what fraction of the time must enhancement 3 be used to achieve an overall speedup of 10?

- Assume the distribution of enhancement usage is 30%, 30%, and 20% for enhancements 1, 2, and 3, respectively.  Assuming all three enhancements are in use, for what fraction of the reduced execution time is no enhancement in use?

- Assume for some benchmark, the fraction of use is 15% for each of the enhancements 1 and 2 and 70% for enhancement 3.  We want to maximize performance.  If only one enhancement can be implemented, which should be chosen?

•	True or false; in general linear speed up is needed to make parallel systems (multiprocessors) cost effective (justify your answer).

•	CPU time (T) is defined as:

T = Ic* CPI * (

Ic stands for the instruction count,

CPI stands for average clock cycles per instruction, and

( stands for the clock cycle time.

A RISC computer, ideally, should be able to execute one instruction per clock cycles.  Within the scope of a RISC architecture, name and discuss (briefly) distinct issues that do not allow ideal performance.