CpE5110/CS5700

Homework #7

1)	Under what circumstances is a k-stage pipeline k times faster than a serial machine, why?

2)	A typical RISC machine requires 4 cycles (fetch, compute address, load, and out result away) for LOAD and STORE instructions, and 3 cycles (fetch, execute, put result away) for each of the other instructions.  Consider the following program:

LOAD			R1  X

SUBTRACT		R1  R1 - R2

STORE			X  R1

ADD				R2  R1 + R2

Draw a timing diagram showing the execution time of these four instructions, and calculate the execution time.  Assume the maximum instruction overlap.

3)	Consider a machine that has multiple execution units (like CDC).  Table 1 shows the Timing table in such organization for the following expression: Y=AX2+B.  Fill out the entries (one for CDC6600 and one for CDC 7600) and explain your reasoning.

ISSUE:		Relative time of instruction issue

START:		Start of function

RESULT:		Function complete with result available

UNIT READY:	Unit ready for reuse

FETCH:		Operand fetched from storage and available in x register

STORE:		Result stored in storage

Table-1:	Timing Diagram for Y=AX2+B

|  |  |  | inst. |  |  |  | unit |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Word # |  |  | type | issue | start | result | ready | fetch | store |
| N1 | A1=A1+k1 | Fetch x | Long |  |  |  |  |  |  |
|  | A2=A2+k2 | Fetch A | Long |  |  |  |  |  |  |
| N2 | x0=x1*x1 | Form x2 | Short |  |  |  |  |  |  |
|  | x6=x0*x2 | Form Ax2 | Short |  |  |  |  |  |  |
|  | A3=A3+k3 | Fetch B | Long |  |  |  |  |  |  |
| N3 | x7=x6+x3 | Form Y | Short |  |  |  |  |  |  |
|  | A7=A7+k4 | Store Y | Long |  |  |  |  |  |  |

4)	Given the following assembly code.  Exploit the maximum degree of parallelism among the 16 instructions, assuming no resource conflicts and availability of multiple functional units.  For simplicity, no pipelining is assumed, all instructions take one machine cycle to execute, and ignore all other overhead.

a)	Draw the program graph to show the follow relationships among the 16 instruction nodes.

b)	Show scheduling of the program to execute this program in minimum time, assume a three-issue superscalar processor— the processor can issue one memory-access instruction, one add/subtract instruction, and one multiply instruction per cycle.

1)	LOAD		R1, A			9)	MUL		R8, R7, R4

2)	LOAD		R2, B			10)	LOAD	R9, E

3)	MUL		R3, R1, R2		11)	Add		R10, R8, R9

4)	LOAD		R4, D			12)	STORE	Y, R10

5)	MUL		R5, R1, R4		13)	ADD		R11, R6, R10

6)	ADD		R6, R3, R5		14)	STORE	U, R11

7)	STORE		X, R6			15)	SUB		R12, R6, R10

8)	LOAD		R7, C			16)	STORE	V, R12