CpE5110/CS5700

Homework #2

1)	Multiply the following 2s complement operands using the add-and-shift scheme:

a)	A (multiplicand)		= 1011		b)	A (multiplicand)	= 1101

B (multiplier)		= 1001			B (multiplier)		= 0111

2)	Use the Booth's algorithm to multiply the following numbers:

a)	A (multiplicand)	= 10111		b)	A (multiplicand)	= 110111

B (multiplier)	= 11101			B (multiplier)		= 101011

3)	Realize the hardware (gate level design) for the carry look ahead scheme 2 (CLA2) as discussed in the class.  Note, the gates have a fan-in of two, the maximum delay of CLA2 is 5t, and a cascade of 2 CLA2s overlaps 1t operation.  Explain your logic.

4)	Assume carry look ahead is a combinational device of 5 levels of logic attached to a cascade of 4-bit full-adders (Problem #3).  It requires the same input as the 4-bit full adder does, and generates 1 output (e.g., carry out).  Furthermore, it requires the "carry in" at the second level of logic:

a)	Calculate the execution time of a 32-bit parallel adder augmented by the above carry look ahead boxes.

b)	Design a fast adder unit based on the carry look ahead (as above) and carry select concepts.  Calculate the execution time of your design for a 32-bit adder.

- Prove the correctness of modified Booth algorithm (group of Four bits).  Hint:  use the Booth's algorithm.